## Slide 1: Bipolar Transistors
www.pfnicholls.com
AIM:
To understand how bipolar transistor can be used as transducer drivers (including calculations)
PRIOR KNOWLEDGE:
Output transducers, current in circuits, calculating resistor values, calculating power, silicon diodes

## Slide 2
A bipolar transistor has 3 leads called the BASE, COLLECTOR and EMITTER.
A bipolar transistor behaves as a switch.
A small current from a logic gate or other circuit can be used to control a more powerful output transducer.
The device should be called an “npn bipolar transistor” to be completely correct.
Current comes out of the EMITTER
Current flows into the COLLECTOR
COLLECTOR
EMITTER
(The One with the arrow)
BASE
Bipolar Transistor Basics

## Slide 3
Bipolar Transistor Basics (2)
Some common bipolar transistors used are:
BC107 (low power)
BC441, BFY51, 2N3053
TIP31 (plastic package)
NOTE: The collector is usually attached to the metal case or the metal heatsink so take care. The emitter is identified by a tag on metal can style cases. Always check the datasheet.

## Slide 4
Bipolar Transistor Basics (3)
When there is no current in the BASE, no current can flow from the COLLECTOR to the EMITTER
When a small current (IB) flows in the BASE, a much larger current (IC) can flow from COLLECTOR to EMITTER
Small BASE current (IB)
Large COLLECTOR current (IC)
When a the transistor conducts and a current flows into the BASE, the voltage across the BASE-EMITTER junction is 0.7 V
0.7 V

## Slide 5
Using Bipolar Transistors
When used as a transducer driver:
The EMITTER is connected to 0 V
The COLLECTOR is connected to the transducer
The BASE is connected to whatever is controlling the transistor
A BASE resistor is necessary to limit the current into the BASE.
12 V
0 V
RB
BASE Resistor
12 v bulb being controlled by the transistor
Small current in BASE turns on the transistor

## Slide 6
Using Bipolar Transistors (2)
When used as a transducer driver with electric motors, relays or any device containing a coil a protection diode must be used
When the motor turns OFF a large backwards voltage is produced. Called “back EMF”
The back EMF can destroy the transistor
The diode limits the back EMF to 0.7 V which is a safe voltage and so protects the transistor
12 V
0 V
M
Diode in reverse Bias

## Slide 7
Calculating the Gain
The current gain of a transistor is an number that tells us how big the COLLECTOR current is compared to the BASE current.
The symbol for current gain is hFE
The equation for current gain is hFE = IC / IB
The current gain depends on the type of transistor used
12 V
0 V
RB
20 W
Example:
For the transistor shown, current gain = 200, what base current is required?
Solution:
Calculate the COLLECTOR current using the information given about the bulb
P = V I so I = P / V
IC = 20 / 12 = 1.67 A
Calculate the BASE Current knowing the gain equation
hFE = IC / IB
200 = 1.67 / IB
IB = 0.0083 A = 8.3 mA

## Slide 8
Calculating the base resistor
To calculate the base resistor we need to know the current flowing into the base and the voltage across the resistor.
Use R = V / I
12 V
0 V
RB
20 W
IB = 8.3 mA
Voltage from previous circuit = 5 V
Example: A logic gate gives a voltage of 5 V which is used to turn on the transistor in the previous example.
What size of base resistor is needed?
Solution:
The transistor is conducting so BASE-EMITTER voltage = 0.7 V
Calculate the voltage across the BASE resistor
VB = 5.0 – 0.7 = 4.3 V
Calculate RB
RB = 4.3 / 0.0083
RB = 516 Ω
Use lower value from those available
RB = 470 Ω
4.3 V
5 V
0.7 V

## Slide 9
Using Datasheets
Datasheets, such as the one shown below, are available online but they contain A LOT of information.
Look for the main features:
Max power before you need a new one
Max collector current – an important value
Maximum Collector to Emitter voltage when not turned on

## Slide 10
Bipolar transistors vs MOSFETs
MOSFET | BIPOLAR TRANSISTOR
MOSFETs require a VOLTAGE at the GATE to allow them to conduct | Bipolar transistors require a CURRENT flowing into the BASE to allow them to conduct
No current flows into the GATE MOSFETs have a very high input resistance | Current flows into the BASE The base resistance is not very high
Very easy to use – no calculations required | Need a base resistor. Calculations of base resistor and gain are needed to ensure correct operation
Require about 3 V to turn them on Cannot be used with low voltage battery operated circuits | Need 0.7 V to turn them on and so can be used with low voltage battery operated circuits
Easily damaged by static | Quite robust and not easily damaged

## Slide 11
VIN vs VOUT
VIN is the voltage applied to the base resistor
VOUT is measured between the Collector and Emitter
VOUT is also called VCE
Region 1: VIN is less than 0.7 V. The transistor is off. No current flows through the load resistor. The potential difference across the load resistor is zero (V = IR and I = 0). The voltage at the collector is the same as the supply voltage. VCE = Vsupply
When VIN is LOW, VOUT is HIGH

## Slide 12
VIN vs VOUT
The circuit shows how VIN can be varied using a potentiometer
Voltmeters are used to measure VIN and VCE
Region 2: VIN is greater than 0.7 V. Current flows through the Base resistor. Current flows through the load resistor into the Collector. There is a potential difference across the load resistor (V = IR and I ≠ 0)
VCE = Vsupply – Vload
Current flows through the transistor. There is a voltage between the Collector and Emitter. The transistor dissipates energy – it gets hot

## Slide 13
VIN vs VOUT
When used as a transducer driver the transistor should operate in region 3 with enough base current to ensure VCE = 0
Region 3: VIN is greater than 0.7 V. Enough current flows through the Base resistor to allow enough current to flow through the load resistor to make the potential difference equal to the supply voltage. Vload = Vsupply and VCE = 0
No (or minimal) power is dissipated. The transistor is saturated and current is only limited by the load resistor

## Slide 14
VIN vs IC
VIN is the voltage applied to the Base resistor
IC is the current flowing through the load resistor and into the Collector
Region 1: VIN is less than 0.7 V. There is no potential difference across the Base resistor. No current flows into the Base
The transistor is OFF and does not conduct
No current flows through the transistor. IC = 0

## Slide 15
VIN vs IC
The circuit shows how VIN is varied with a potentiometer
A voltmeter measures VIN and an ammeter measures IC
Region 2: VIN is greater than 0.7 V. VBE = 0.7 V. There is a potential difference across the Base resistor. Current flows into the Base and therefore current flows into the Collector. IC ≠ 0
As VIN increases, the potential difference across the Base resistor increases. The current flowing into the Base increases and therefore the Collector current increases. VIN↑  IC↑

## Slide 16
VIN vs IC
When used as a transducer driver the Base current should be great enough to allow the transistor to operate in region 3
Region 3: VIN is greater than 0.7 V. The transistor is saturated
VCE = 0 and the current is only limited by the load resistor. The load resistor is fixed and so IC has reached a maximum value
VIN increases but IC does not change

## Slide 17
IB vs IC
IB is the current flowing into the Base
IC is the current flowing into the Collector
Region 1: The Collector current increases as the Base current increases. The relationship is linear
IC is directly proportional to IB
IC = hFE x IB

## Slide 18
IB vs IC
The circuit shows how ammeters can be used to measure IB and IC
Region 2: The transistor is saturated and the current is limited by the load resistor
IB increases but IC remains constant

## Slide 19
Summary
NPN Bipolar transistors have a BASE, COLLECTOR and EMITTER and can be used as a switch. They need a BASE resistor to limit the current flowing into the BASE.
When BASE-EMITTER voltage = 0.7 V and current flows into the BASE then a large current can flow from COLLECTOR to EMITTER
The Gain equation is hFE = IC / IB and hFE is typically ≈ 100 but this value depends on the transistor being used
Protection diodes must be used when switching loads with a coil such as motors, heaters and relays
Maximum ratings of current, voltage and power must be researched using online datasheets and these values are different for each transistor
Transistors can get hot if they dissipate too much power and so a heatsink might be necessary where high power output transducers are used

## Slide 20
Questions
An npn bipolar transistor has a collector current of 5 A and needs a base current of 400 mA. What is the gain of the transistor?
An npn transistor needs a base current of 20 mA and the base resistor is attached to a 9 V battery. What value of base resistor should be used?
An npn bipolar transistor is used to switch on a load when it receives a signal from a control circuit. The transistor has a current gain of 200. If the output from the control circuit is 12 V and the current required by the load is 400 mA, what value of base resistor is needed?

## Slide 21
Answers
hFE = IC / IB IC = 5 A and IB = 0.4 A (note change of units)
  hFE = 5 / 0.4 = 12.5 (there are no units)
When transistor conducts, the BASE voltage is 0.7 V
  The voltage across resistor = 9 V – 0.7 V = 8.3 V
  BASE current = 20 mA so R = 8.3 / 0.02 = 415 Ω so use 390 Ω
The gain equation gives a BASE current of 400 mA / 200 = 2 mA
  BASE voltage of 0.7 V means that there is a voltage across the BASE resistor of 12 V – 0.7 V = 11.3 V
  Therefore, R = 11.3 / 0.002 = 5650 Ω so use 5600 Ω